Appendix 3

Vapor Recovery Health and Safety Code Statutes

H&S 41950 Vapor Recovery Systems for Stationary Gas Tanks

41950. (a) Except as provided in subdivisions (b) and (e), no

person shall install or maintain any stationary gasoline tank with a

capacity of 250 gallons or more which is not equipped for loading

through a permanent submerged fill pipe, unless such tank is a pressure

tank as described in Section 41951, or is equipped with a vapor

recovery system as described in Section 41952 or with a floating roof

as described in Section 41953, or unless such tank is equipped with

other apparatus of equal efficiency which has been approved by the air

pollution control officer in whose district the tank is located.

(b) Subdivision (a) shall not apply to any stationary tanks

installed prior to December 31, 1970.

(c) For the purpose of this section, "gasoline" means any

petroleum distillate having a Reid vapor pressure of four pounds or

greater.

(d) For the purpose of this section, "submerged fill pipe"

means any fill pipe which has its discharge opening entirely submerged

when the liquid level is six inches above the bottom of the tank.

"Submerged fill pipe," when applied to a tank which is loaded

from the side, means any fill pipe which has its discharge opening

entirely submerged when the liquid level is 18 inches above the bottom

of the tank.

(e) Subdivision (a) shall not apply to any stationary tank which is

used primarily for the fueling of implements of husbandry.

(Added by Stats. 1975, Ch. 957.)

H&S 41951 Definition of Pressure Tank

41951. A "pressure tank" is a tank which maintains working

pressure sufficient at all times to prevent hydrocarbon vapor or gas

loss to the atmosphere.

(Added by Stats. 1975, Ch. 957.)

H&S 41952 Definition of Vapor Recovery System

41952. A "vapor recovery system" consists of a vapor

gathering system capable of collecting the hydrocarbon vapors and gases

discharged and a vapor disposal system capable of processing such

hydrocarbon vapors and gases so as to prevent their emission into the

atmosphere, with all tank gauging and sampling devices gastight except

when gauging or sampling is taking place.

(Added by Stats. 1975, Ch. 957.)

H&S 41953 Definition of Floating Roof

41953. A "floating roof" consists of a pontoon-type or

double-deck-type roof, resting on the surface of the liquid contents

and equipped with a closure seal, or seals, to close the space between

the roof edge and tank wall. The control equipment required by this

section shall not be used if the gasoline or petroleum distillate has a

vapor pressure of 11.0 pounds per square inch absolute or greater under

actual storage conditions. All tank gauging and sampling devices shall

be gastight except when gauging or sampling is taking place.

(Added by Stats. 1975, Ch. 957.)

H&S 41954 ARB Shall Certify Vapor Recovery Systems

41954. (a) The state board shall adopt procedures for determining

the compliance of any system designed for the control of gasoline vapor

emissions during gasoline marketing operations, including storage and

transfer operations, with performance standards that are reasonable and

necessary to achieve or maintain any applicable ambient air quality standard.

(b) The state board shall, after a public hearing, adopt additional

performance standards that are reasonable and necessary to ensure that

systems for the control of gasoline vapors resulting from motor vehicle

fueling operations do not cause excessive gasoline liquid spillage and

excessive evaporative emissions from liquid retained in the dispensing

nozzle or vapor return hose between refueling events, when used in a

proper manner. To the maximum extent practicable, the additional

performance standards shall allow flexibility in the design of gasoline

vapor recovery systems and their components.

(c) (1) The state board shall certify, in cooperation with the

districts, only those gasoline vapor control systems that it determines

will meet the following requirements, if properly installed and

maintained:

(A) The systems will meet the requirements of subdivision (a).

(B) With respect to any system designed to control gasoline vapors

during vehicle refueling, that system, based on an engineering

evaluation of that system's component qualities, design, and test

performance, can be expected, with a high degree of certainty, to

comply with that system's certification conditions over the warranty

period specified by the board.

(C) With respect to any system designed to control gasoline vapors

during vehicle refueling, that system shall be compatible with vehicles

equipped with onboard refueling vapor recovery (ORVR) systems.

(2) The state board shall enumerate the specifications used for

issuing the certification. After a system has been certified, if

circumstances beyond the control of the state board cause the system to

no longer meet the required specifications or standards, the state

board shall revoke or modify the certification.

(d) The state board shall test, or contract for testing, gasoline

vapor control systems for the purpose of determining whether those

systems may be certified.

(e) The state board shall charge a reasonable fee for

certification, not to exceed its actual costs therefor. Payment of the

fee shall be a condition of certification.

(f) No person shall offer for sale, sell, or install any new or

rebuilt gasoline vapor control system, or any component of the system,

unless the system or component has been certified by the state board

and is clearly identified by a permanent identification of the

certified manufacturer or rebuilder.

(g) (1) Except as authorized by other provisions of law and except

as provided in this subdivision, no district may adopt, after July 1,

1995, stricter procedures or performance standards than those adopted

by the state board pursuant to subdivision (a), and no district may

enforce any of those stricter procedures or performance standards.

(2) Any stricter procedures or performance standards shall not

require the retrofitting, removal, or replacement of any existing

system, which is installed and operating in compliance with applicable

requirements, within four years from the effective date of those

procedures or performance standards, except that existing requirements

for retrofitting, removal, or replacement of nozzles with nozzles

containing vapor-check valves may be enforced commencing July 1, 1998.

(3) Any stricter procedures or performance standards shall not be

implemented until at least two systems meeting the stricter performance

standards have been certified by the state board.

(4) If the certification of a gasoline vapor control system, or a

component thereof, is revoked or modified, no district shall require a

currently installed system, or component thereof, to be removed for a

period of four years from the date of revocation or modification.

(h) No district shall require the use of test procedures for

testing the performance of a gasoline vapor control system unless those

test procedures have been adopted by the state board or have been

determined by the state board to be equivalent to those adopted by the

state board, except that test procedures used by a district prior to

January 1, 1996, may continue to be used until January 1, 1998, without

state board approval.

(i) With respect to those vapor control systems subject to

certification by the state board, there shall be no criminal or civil

proceedings commenced or maintained for failure to comply with any

statute, rule, or regulation requiring a specified vapor recovery

efficiency if the vapor control equipment which has been installed to

comply with applicable vapor recovery requirements meets both of the

following requirements:

(1) Has been certified by the state board at an efficiency or

emission factor required by applicable statutes, rules, or regulations.

(2) Is installed, operated, and maintained in accordance with the

requirements set forth in the document certification and the

instructions of the equipment manufacturer.

(Amended by Stats. 2000, Ch. 729, Sec. 14.)

References at the time of publication (see page iii):

Regulations:

17, CCR, sections 94006, 94010, 94011,

94012, 94013, 94014, 94015, 94148, 94149, 94150, 94151, 94152, 94153,

94154, 94155, 94156, 94157, 94158, 94159, 94160, 94163

H&S 41955 Certification Required by Other Agencies

41955. Prior to state board certification of a gasoline vapor

control system pursuant to Section 41954, the manufacturer of the

system shall submit the system to, or, if appropriate, the components

of the system as requested by, the Division of Measurement Standards of

the Department of Food and Agriculture and the State Fire Marshal for

their certification.

(Added by Stats. 1976, Ch. 1030.)

H&S 41956 Other Agencies to Adopt Rules for Certification

41956. (a) As soon as possible after the effective date of this

section, the State Fire Marshal and the Division of Measurement

Standards, after consulting with the state board, shall adopt rules and

regulations for the certification of gasoline vapor control systems and

components thereof.

(b) The State Fire Marshal shall be the only agency responsible for

determining whether any component or system creates a fire hazard. The

division shall be the only agency responsible for the measurement

accuracy aspects, including gasoline recirculation of any component or

system.

(c) Within 120 days after the effective date of this subdivision,

the Division of Measurement Standards, shall, after public hearing,

adopt rules and regulations containing additional performance standards

and standardized certification and compliance test procedures which are

reasonable and necessary to prevent gasoline recirculation in systems

for the control of gasoline vapors resulting from motor vehicle fueling

operations.

(Amended by Stats. 1981, Ch. 902.)

H&S 41956.1 Revision of Standards for Vapor Recovery Systems

41956.1. (a) Whenever the state board, the Division of Measurement

Standards of the Department of Food and Agriculture, or the State Fire

Marshal revises performance or certification standards or revokes a

certification, any systems or any system components certified under

procedures in effect prior to the adoption of revised standards or the

revocation of the certification and installed prior to the effective

date of the revised standards or revocation may continue to be used in

gasoline marketing operations for a period of four years after the

effective date of the revised standards or the revocation of the

certification. However, all necessary repair or replacement parts or

components shall be certified.

(b) Notwithstanding subdivision (a), whenever the State Fire

Marshal determines that a system or a system component creates a hazard

to public health and welfare, the State Fire Marshal may prevent use of

the particular system or component.

(c) Notwithstanding subdivision (a), the Division of Measurement

Standards may prohibit the use of any system or any system component if

it determines on the basis of test procedures adopted pursuant to

subdivision (c) of Section 41956, that use of the system or component

will result in gasoline recirculation.

(Amended by Stats. 1996, Ch. 426, Sec. 2.)

References at the time of publication (see page iii):

Regulations:  17, CCR, section 94011

H&S 41957 Division of Industrial Safety Responsibilities

41957. The Division of Occupational Safety and Health of the

Department of Industrial Relations is the only agency responsible for

determining whether any gasoline vapor control system, or component

thereof, creates a safety hazard other than a fire hazard.

If the division determines that a system, or component thereof,

creates a safety hazard other than a fire hazard, that system or

component may not be used until the division has certified that the

system or component, as the case may be, does not create that hazard.

The division, in consultation with the state board, shall adopt the

necessary rules and regulations for the certification if the

certification is required.

(Amended by Stats. 1981, Ch. 714.)

H&S 41958 Rules Shall Allow for Flexibility in Design

41958. To the maximum extent practicable, the rules and regulations

adopted pursuant to Sections 41956 and 41957 shall allow flexibility in

the design of gasoline vapor control systems and their components. The

rules and regulations shall set forth the performance standards as to

safety and measurement accuracy and the minimum procedures to be

followed in testing the system or component for compliance with the

performance standards.

The State Fire Marshal, the Division of Occupational Safety and

Health, and the Division of Measurement Standards shall certify any

system or component which complies with their adopted rules and

regulations. Any one of the state agencies may certify a system or

component on the basis of results of tests performed by any entity

retained by the manufacturer of the system or component or by the state

agency. The requirements for the certification of a system or component

shall not require that it be tested, approved, or listed by any private

entity, except that certification testing regarding recirculation of

gasoline shall include testing by an independent testing laboratory.

(Amended by Stats. 1982, Ch. 466, Sec. 72.)

H&S 41959 Certification Testing

41959. Certification testing of gasoline vapor control systems and

their components by the state board, the State Fire Marshal, the

Division of Measurement Standards, and the Division of Occupational

Safety and Health may be conducted simultaneously.

(Amended by Stats. 1981, Ch. 714.)

References at the time of publication (see page iii):

Regulations:  17, CCR, sections 94010, 94011, 94012, 94013

H&S 41960 Certification by State Agencies Sufficient

41960. (a) Certification of a gasoline vapor recovery system for

safety and measurement accuracy by the State Fire Marshal and the

Division of Measurement Standards and, if necessary, by the Division of

Occupational Safety and Health shall permit its installation wherever

required in the state, if the system is also certified by the state

board.

(b) Except as otherwise provided in subdivision (g) of Section

41954, no local or regional authority shall prohibit the installation

of a certified system without obtaining concurrence from the state

agency responsible for the aspects of the system which the local or

regional authority disapproves.

(Amended by Stats. 1996, Ch. 426, Sec. 3.)

References at the time of publication (see page iii):

Regulations:  17, CCR, sections 94011, 94012, 94013

H&S 41960.1 Operation in Accordance with Standards

41960.1. (a) All vapor control systems for the control of gasoline

vapors resulting from motor vehicle fueling operations shall be

operated in accordance with the applicable standards established by the

State Fire Marshal or the Division of Measurement Standards pursuant to

Sections 41956 to 41958, inclusive.

(b) When a sealer or any authorized employee of the Division of

Measurement Standards determines, on the basis of applicable test

procedures of the division, adopted after public hearing, that an

individual system or component for the control of gasoline vapors

resulting from motor vehicle fueling operations does not meet the

applicable standards established by the Division of Measurement

Standards, he or she shall take the appropriate action specified in

Section 12506 of the Business and Professions Code.

(c) When a deputy State Fire Marshal or any authorized employee of

a fire district or local or regional firefighting agency determines

that a component of a system for the control of gasoline vapors

resulting from motor vehicle fueling operations does not meet the

applicable standards established by the State Fire Marshal, he or she

shall mark the component "out of order." No person shall use or

permit the use of the component until the component has been repaired,

replaced, or adjusted, as necessary, and either the component has been

inspected by a representative of the agency employing the person

originally marking the component, or the person using or permitting use

of the component has been expressly authorized by the agency to use the

component pending reinspection.

(Added by Stats. 1981, Ch. 902.)

H&S 41960.2 Maintenance of Installed Systems

41960.2. (a) All installed systems for the control of gasoline

vapors resulting from motor vehicle fueling operations shall be

maintained in good working order in accordance with the manufacturer' s

specifications of the system certified pursuant to Section 41954.

(b) Whenever a gasoline vapor recovery control system is repaired

or rebuilt by someone other than the original manufacturer or its

authorized representative, the person shall permanently affix a plate

to the vapor recovery control system that identifies the repairer or

rebuilder and specifies that only certified equipment was used. In

addition, a rebuilder of a vapor control system shall remove any

identification of the original manufacturer if the removal does not

affect the continued safety or performance of the vapor control system.

(c) (1) The executive officer of the state board shall identify

and list equipment defects in systems for the control of gasoline

vapors resulting from motor vehicle fueling operations that

substantially impair the effectiveness of the systems in reducing air

contaminants. The defects shall be identified and listed for each

certified system and shall be specified in the applicable certification

documents for each system.

(2) On or before January 1, 2001, and at least once every three

years thereafter, the list required to be prepared pursuant to

paragraph (1) shall be reviewed by the executive officer at a public

workshop to determine whether the list requires an update to reflect

changes in equipment technology or performance.

(3) Notwithstanding the timeframes for the executive officer's

review of the list, as specified in paragraph (2), the executive

officer may initiate a public review of the list upon a written request

that demonstrates, to the satisfaction of the executive officer, the

need for such a review. If the executive officer determines that an

update is required, the update shall be completed no later than 12

months after the date of the determination.

(d) When a district determines that a component contains a defect

specified pursuant to subdivision (c), the district shall mark the

component "Out of Order." No person shall use or permit the use

of the component until the component has been repaired, replaced, or

adjusted, as necessary, and the district has reinspected the component

or has authorized use of the component pending reinspection.

(e) Where a district determines that a component is not in good

working order but does not contain a defect specified pursuant to

subdivision (c), the district shall provide the operator with a notice

specifying the basis on which the component is not in good working

order. If, within seven days, the operator provides the district with

adequate evidence that the component is in good working order, the

operator shall not be subject to liability under this division.

(Amended by Stats. 1999, Ch. 501, Sec. 1.)

References at the time of publication (see page iii):

Regulations:  17, CCR, sections 94006, 94010, 94011

H&S 41960.3 Telephone Number for Reporting Problems

41960.3. (a) Each district which requires the installation of

systems for the control of gasoline vapors resulting from motor vehicle

fueling operations shall establish a toll free telephone number for use

by the public in reporting problems experienced with the systems.

Districts within an air basin or adjacent air basin may enter into a

cooperative program to implement this requirement. All complaints

received by a district shall be recorded on a standardized form which

shall be established by the state board, in consultation with

districts, the State Fire Marshal, and the Division of Measurement

Standards in the Department of Food and Agriculture. The operating

instructions required by Section 41960.4 shall be posted at all service

stations at which systems for the control of gasoline vapors resulting

from motor vehicle fueling operations are installed and shall include a

prominent display of the toll free telephone number for complaints in

the district in which the station is located.

(b) Upon receipt of each complaint, the district shall diligently

either investigate the complaint or refer the complaint for

investigation by the state or local agency which properly has

jurisdiction over the primary subject of the complaint. When the

investigation has been completed, the investigating agency shall take

such remedial action as is appropriate and shall advise the complainant

of the findings and disposition of the investigation. A copy of the

complaint and response to the complaint shall be forwarded to the state

board.

(Amended by Stats. 1986, Ch. 194, Sec. 1.)

H&S 41960.4 Operating Instructions

41960.4. The operator of each service station utilizing a system

for the control of gasoline vapors resulting from motor vehicle fueling

operations shall conspicuously post operating instructions for the

system in the gasoline dispensing area. The instructions shall clearly

describe how to fuel vehicles correctly with vapor recovery nozzles

utilized at the station and shall include a warning that repeated

attempts to continue dispensing, after the system having indicated that

the vehicle fuel tank is full, may result in spillage or recirculation

of gasoline.

(Added by Stats. 1981, Ch. 902.)

H&S 41960.5 Nozzle Size Requirements

41960.5. (a) No retailer, as defined in Section 20999 of the Business and

Professions Code, shall allow the operation of any gasoline pump from which

leaded gasoline is dispensed, or which is labeled as providing leaded

gasoline, unless the pump is equipped with a nozzle spout meeting the required specifications for leaded gasoline nozzle spouts set forth in Title 40, Code of Federal Regulations, Section 80.22(f)(1).

(b) For the purpose of this section, "leaded gasoline" means gasoline

which is produced with the use of any lead additive or which contains

more than 0.05 gram of lead per gallon or more than 0.005 gram of phosphorus per gallon.

(Added by Stats. 1987, Ch. 592, Sec. 2.)

H&S 41960.6 Fuel Pump Nozzles

41960.6. (a) No retailer, as defined in subdivision (g) of Section

20999 of the Business and Professions Code, shall, on or after July 1,

1992, allow the operation of a pump, including any pump owned or

operated by the state, or any county, city and county, or city,

equipped with a nozzle from which gasoline or diesel fuel is dispensed,

unless the nozzle is equipped with an operating hold open latch. Any

hold open latch determined to be inoperative by the local fire marshal

or district official shall be repaired or replaced by the retailer,

within 48 hours after notification to the retailer of that

determination, to avoid any applicable penalty or fine.

(b) For purposes of this section, a "hold open latch" means

any device which is an integral part of the nozzle and is manufactured

specifically for the purpose of dispensing fuel without requiring the

consumer's physical contact with the nozzle.

(c) Subdivision (a) does not apply to nozzles at facilities which

are primarily in operation to refuel marine vessels or aircraft.

(d) Nothing in this section shall affect the current authority of

any local fire marshal to establish and maintain fire safety provisions

for his or her jurisdiction.

(Added by Stats. 1991, Ch. 468, Sec. 2.)

H&S 41961 Fees for Certification

41961. The State Fire Marshal, the Division of Measurement

Standards, and the Division of Occupational Safety and Health may

charge a reasonable fee for certification of a gasoline vapor control

system or a component thereof, not to exceed their respective estimated

costs therefor. Payment of the fee may be made a condition of

certification. All money collected by the State Fire Marshal pursuant

to this section shall be deposited in the State Fire Marshal Licensing

and Certification Fund established pursuant to Section 13137, and shall

be available to the State Fire Marshal upon appropriation by the

Legislature to carry out the purposes of this article.

(Amended by Stats. 1992, Ch. 306, Sec. 5. Effective January 1, 1993.

Operative July 1, 1993, by Sec. 6 of Ch. 306.)

H&S 41962 Vapor Recovery Systems on Cargo Tank Vehicles

41962. (a) Notwithstanding Section 34002 of the Vehicle Code, the

state board shall adopt test procedures to determine the compliance of

vapor recovery systems of cargo tanks on tank vehicles used to

transport gasoline with vapor emission standards which are reasonable

and necessary to achieve or maintain any applicable ambient air quality

standard. The performance standards and test procedures adopted by the

state board shall be consistent with the regulations adopted by the

Commissioner of the California Highway Patrol and the State Fire

Marshal pursuant to Division 14.7 (commencing with Section 34001) of

the Vehicle Code.

(b) The state board may test, or contract for testing, the vapor

recovery system of any cargo tank of any tank vehicle used to transport

gasoline. The state board shall certify the cargo tank vapor recovery

system upon its determination that the system, if properly installed

and maintained, will meet the requirements of subdivision (a). The

state board shall enumerate the specifications used for issuing such

certification. After a cargo tank vapor recovery system has been

certified, if circumstances beyond control of the state board cause the

system to no longer meet the required specifications, the certification

may be revoked or modified.

(c) Upon verification of certification pursuant to subdivision (b),

which shall be done annually, the state board shall send a verified

copy of the certification to the registered owner of the tank vehicle,

which copy shall be retained in the tank vehicle as evidence of

certification of its vapor recovery system. For each system certified,

the state board shall issue a nontransferable and nonremovable decal to

be placed on the cargo tank where the decal can be readily seen.

(d) With respect to any tank vehicle operated within a district,

the state board, upon request of the district, shall send to the

district, free of charge, a certified copy of the certification and

test results of any cargo tank vapor recovery system on the tank

vehicle.

(e) The state board may contract with the Department of the

California Highway Patrol to carry out the responsibilities imposed by

subdivisions (b), (c), and (d).

(f) The state board shall charge a reasonable fee for

certification, not to exceed its estimated costs therefor. Payment of

the fee shall be a condition of certification. The fees may be

collected by the Department of the California Highway Patrol and

deposited in the Motor Vehicle Account in the State Transportation

Fund. The Department of the California Highway Patrol shall transfer to

the Air Pollution Control Fund the amount of those fees necessary to

reimburse the state board for the costs of administering the

certification program.

(g) No person shall operate, or allow the operation of, a tank

vehicle transporting gasoline and required to have a vapor recovery

system, unless the system thereon has been certified by the state board

and is installed and maintained in compliance with the state board's

requirements for certification. Tank vehicles used exclusively to

service gasoline storage tanks which are not required to have gasoline

vapor controls are exempt from the certification requirement.

(h) Performance standards of any district for cargo tank vapor

recovery systems on tank vehicles used to transport gasoline shall be

identical with those adopted by the state board therefor and no

district shall adopt test procedures for, or require certification of,

cargo tank vapor recovery systems. No district may impose any fees on,

or require any permit of, tank vehicles with vapor recovery systems.

However, nothing in this section shall be construed to prohibit a

district from inspecting and testing cargo tank vapor recovery systems

on tank vehicles for the purposes of enforcing this section or any rule

and regulation adopted thereunder that are applicable to such systems

and to the loading and unloading of cargo tanks on tank vehicles.

(i) The Legislature hereby declares that the purposes of this

section regarding cargo tank vapor recovery systems on tank vehicles

are (1) to remove from the districts the authority to certify, except

as specified in subdivision (b), such systems and to charge fees

therefor, and (2) to grant such authority to the state board, which

shall have the primary responsibility to assure that such systems are

operated in compliance with its standards and procedures adopted

pursuant to subdivision (a).

(Amended by Stats. 1982, Ch. 1255, Sec. 2. Operative July 1, 1983,

or earlier, by Sec. 27.5 of Ch. 1255.)

References at the time of publication (see page iii):

Regulations:  17, CCR, sections 94014, 94015