ATTACHMENT A

MAPS AND TABLES OF THE AREA DESIGNATIONS FOR STATE AND NATIONAL

AMBIENT AIR QUALITY STANDARDS

ATTACHMENT A

MAPS AND TABLES OF THE AREA DESIGNATIONS

FOR STATE AND NATIONAL AMBIENT AIR QUALITY STANDARDS

A.		 INTRODUCTION

This attachment fulfills the requirement of Health and Safety Code, section 40718 for the Air Resources Board (the Board) to publish maps that identify where one or more violations of any State or federal ambient air quality standard have been measured.  Federal standards are the National Ambient Air Quality Standards promulgated under section 109 of the federal Clean Air Act (42 U.S.C. 7409).

The attachment is divided into three sections.  Section 1 details the levels and specific requirements of both the State and the national ambient air quality standards.

Section 2 contains maps and tables showing the area designations for each pollutant for which there is a State ambient air quality standard (State standard).  These maps and summary tables reflect the proposed amendments to the area designations that the Board will consider in November 1997, pursuant to Health and Safety Code section 39608.  An attainment designation indicates that pollutant concentrations in the area did not violate the State standard for that pollutant, excluding exceedances affected by highly irregular or infrequent events as defined in Appendix 2 to the designation criteria.  A nonattainment designation indicates that a pollutant concentration did violate the State standard at least once during the previous three calendar years.  Again, exceedances affected by highly irregular or infrequent events are excluded.  An unclassified designation indicates that air quality and other relevant information is insufficient to determine whether the area is attainment or nonattainment.  In addition to these three major designation categories, there is a subcategory of the nonattainment designation called nonattainment-transitional.  This subcategory applies to areas that are close to attainment and meet other conditions as specified in the designation criteria.

Section 3 contains maps and summary tables showing the area designations for each pollutant for which there is a national ambient air quality standard (national standard).  These area designations have been promulgated as final by the United States Environmental Protection Agency (U.S. EPA) based on the requirements in section 107(d) of the Clean Air Act as amended in 1990 (42 U.S.C. 7407(d)).

1. 	State and National Ambient Air Quality Standards

The Board has adopted and the U.S. EPA has promulgated ambient air quality concentration levels that define good air quality.  These levels are the ambient air quality standards and were established to protect human health and/or welfare.  The levels of the State and national standards may differ because the Board and the U.S. EPA considered different bodies of information, and the Board chose to provide a wider margin of safety in the State standards than did the U.S. EPA in the national standards.

An ambient air quality standard is a concentration level expressed in either parts per million or micrograms per cubic meter and averaged over a specific time period such as one-hour, eight-hours, 24-hours, or one year.  The different averaging times and concentrations are meant to protect against different exposure effects.  Some ambient air quality standards are expressed as a concentration that is not to be exceeded.  Others are expressed as a concentration that is not to be equaled or exceeded.

The national standards are further categorized as primary standards and secondary standards.  The primary national standards are meant to protect public health.  The secondary national standards are meant to protect the public welfare from any known or anticipated adverse effects of the pollutant.

The following table contains information for both the State standards and the national standards.  Specifically, the table lists the applicable pollutant levels, averaging times, and analytical measurement methods.

NOTES FOR AMBIENT AIR QUALITY STANDARDS TABLE

1.	 State standards for ozone, carbon monoxide (except the Lake Tahoe Air Basin), sulfur dioxide, nitrogen dioxide, suspended particulate matter (PM10), and visibility reducing particles are values that are not to be exceeded.  The State standards for sulfates, Lake Tahoe Air Basin carbon monoxide, lead, hydrogen sulfide, and vinyl chloride are not to be equaled or exceeded.

2.	National standards, other than ozone and those based on annual averages or annual arithmetic means, are not to be exceeded more than once a year.  The ozone standard is attained when the expected number of days per calendar year with maximum hourly average concentrations above the standard is equal to or less than one.

3.	Concentration expressed first in units in which it was promulgated.  Equivalent units, given in parentheses, are based upon a reference temperature of 25 degrees C and a reference pressure of 760 mm of mercury.  All measurements of air quality are to be corrected to a reference temperature of 25 degrees C and a reference pressure of 760 mm of mercury (1013.2 millibar); ppm (parts per million) in this table refers to ppm by volume, or micro moles of pollutant per mole of gas.

4.	Any equivalent procedure which can be shown to the satisfaction of the Air Resources Board to give equivalent results at or near the level of the air quality standard may be used.

5.	National Primary Standards:  The level of air quality necessary, with an adequate margin of safety, to protect public health.

6.	National Secondary Standards:  The level of air quality necessary to protect the public welfare from any known or anticipated adverse effects of a pollutant.

7. 	Reference method as described by the U.S. EPA.  An equivalent method of measurement may be used but must have a consistent relationship to the reference method and must be approved by the U.S. EPA.

8.	On July 16, 1997 U.S. EPA adopted new national standards for ozone, PM10, and PM 2.5.  The new standards were published in the Federal Register on July 18, 1997.  The designations based on the new standards for ozone and PM10 are expected to occur in September 2000, and for PM 2.5 after September 2002.  The schedule for the implementation plan of these new standards is expected to be available on September 16, 1997.

9.	This standard is intended to limit the frequency and severity of visibility impairment due to regional haze and is equivalent to a 10-mile nominal visual range when the relative humidity is less than 70 percent.

10. 	This standard is equivalent to a 30-mile nominal visual range when the relative humidity is less than 70 percent.

2.	 Area Designations for the State Ambient Air Quality Standards

This section contains a description of the area designations for each pollutant for which there is a State ambient air quality standard listed in the California Code of Regulations, Title 17, section 70200.  The information presented reflects the proposed amendments to the area designations that the Board will consider in November 1997.

The area designations for each pollutant are presented in the form of a map and also, a summary table.  Areas are identified as attainment, nonattainment, nonattainment-transitional, or unclassified for each pollutant, as shown, below:

Attainment	A

Nonattainment	N

Nonattainment-Transitional	T

Unclassified	U

Generally, the Board designates areas by air basin or county.  However, when there are areas of an air basin or county with distinctly different air quality deriving from sources and conditions not affecting the entire air basin or county, the Board may designate a smaller area.  Generally, when the boundaries of the designated area differ from the air basin or county boundaries, the description of the specific area is referenced at the bottom of the summary table.

3. 	Area Designations for the National Ambient Air Quality Standards

This section contains a description of the area designations for each pollutant for which there is a national ambient air quality standard, except lead.  The national lead standard was promulgated after the Federal Clean Air Act was amended in 1977, and in promulgating the national lead standard, the United States Environmental Protection Agency (U.S. EPA) did not require areas to be designated in a manner similar to other pollutants.  The area designations for each pollutant are presented in the form of a map and also, a summary table.

The U.S. EPA uses two categories to designate areas with respect to ozone, carbon monoxide, and nitrogen dioxide.  These designation categories are:

o Does not meet primary standards, and

o Cannot be classified or better than national standards.

Areas that do not meet the primary national standards for these pollutants are indicated on the following maps and summary tables as N for nonattainment.  Areas that cannot be classified or are better than the national standards are indicated as UA" for unclassified/attainment.

The U.S. EPA uses four categories to designate areas with respect to sulfur dioxide.  These designation categories are:

o Does not meet the primary standards,

o Does not meet the secondary standards,

o Cannot be classified, and

o Better than the national standards.

In California, the first two designation categories listed above do not apply.  The map and summary table for sulfur dioxide show areas that cannot be classified as U for unclassifiable and areas that are better than the national standards as A for attainment.

Finally, the U.S. EPA uses two categories to designate areas with respect to suspended particulate matter (PM10).  These designation categories are:

o Nonattainment, and

o Unclassifiable.

The map and summary table for the national PM10 standards indicate N for areas designated as nonattainment and U for areas that cannot be classified.

From time to time, the boundaries of the California air basins have been changed to facilitate the planning process.  The Board generally initiates these changes, and they are not always reflected in the U.S. EPA area designations.  For purposes of consistency with Section 2 of this attachment, all of the maps in the following section reflect the current air basin boundaries as adopted by the Board.  Specifically, the maps show the western portion of Placer County as being in the Sacramento Valley Air Basin while the national area designations identify the western portion of Placer County as being in the Mountain Counties Air Basin.  Also, while the national area designations reflect the former Southeast Desert Air Basin, the maps in this section show the new Mojave Desert and Salton Sea Air Basin boundaries which were established by the Board in 1997, in accordance with H&SC, section 39606.1.  Nevertheless, the summary tables in this section reflect the area designations as promulgated by the U.S. EPA.