Appendix E

# Air Quality Modeling of Emissions from 
Thermal Spraying Operations

# Air Quality Modeling of Emissions from Thermal Spraying Operations

Prepared by:  Tony Servin, P.E.,

Planning and Technical Support Division,

California Air Resources Board,

California Environmental Protection Agency

Date:		 September 22, 2004	DRAFT

###### Summary

It is requested to evaluate air quality impacts from emissions of hexavalent chromium from thermal spray operations.  Four separate facilities are evaluated with meteorological data from different regions in the State.  The emissions from the facilities range from 0.00011 lbs/yr to 0.023 lbs/yr.  The maximum above ambient annual average concentration is estimated to be 2.8x10-4 μg/m3 from the facility emitting 0.023 lbs/yr hexavalent chromium.  Details of the analysis and additional results are described below.

### Approach

Data from four separate facilities in the San Diego AQMD which have hexavalent chromium emissions are evaluated on an annual average basis for downwind air impacts.  The stack parameters and building configurations are input to the US-EPA ISCST3 (Version 02035) air quality model to estimate downwind impacts.  Urban dispersion coefficients are used in ISCST3.  Receptor heights are set at 1.2 meters above ground level.  Terrain is assumed to be flat.  Meteorological data are considered from locations that are closest to each facility and as well as data from other places in the State such as Vernon, West Los Angeles, and South San Francisco.

## Inputs

Tables 1 and 2 summarize the model inputs for the source configurations as derived from data provided by SSD staff.

| Table 1 – Volume Sources |
| --- |
| ID | H (m) | Syo (m) | Szo (m) | Bw (m) | Bh (m) |
| Src1 | 1.8 | 9.9 | 2.3 | 42.6 | 4.9 |
| Syo=L/4.3, Szo=H/2.15. Bw is taken as the length of the shortest side of the building. |

| Table 2 – Point Sources |
| --- |
| ID | Hs (m) | Ts (K) | Vs (m/s) | Ds (m) | Bw (m) | Bh(m) | Notes |
| Src2 | 5.5 | 299.8 | 23.96 | 0.549 | 43 | 4.0 | (a) |
| Src3 | 10.7 | 294.3 | 19.01 | 0.811 | 100 | 9.2 | (b) |
| Src4 | 13.7 | 293.2 | 12.92 | 0.884 | 181 | 12.2 | (c) |
| Bh estimated at 1.5 meters below Hs. Bw is estimated as the diameter of equivalent area to footprint. Bh estimated at 1.5 meters below Hs. Bw is estimated as the average of the other three facilities. Source next to Magnolia School. Bh is given. Bw is estimated as the diameter of equivalent area to footprint. |

The annual average emissions are uniformly distributed over all hours when emissions may result.  Even though facilities may only emit hexavalent chromium during certain periods (e.g., two hours per day), it is assumed that emissions may occur anytime the facility is in operation.  Provided emissions result throughout the operating period over the year, this assumption should not bias the results.  Table 3 below shows the annual inventory and the hours over which the annual average emissions are uniformly distributed based on data obtained on the operations of each facility.

| Table 3 – Annual Inventory and Hourly Distribution |
| --- |
| ID | Annual Inventory (lbs/yr) | Hours when Emissions may Occur |
|  |  | Hours per day | Beginning at |
| Src1 | 2.27E-02 | 9 | 8 am |
| Src2 | 2.85E-04 | 6 | 6 am |
| Src3 | 2.78E-03 | 24 | - |
| Src4 | 1.10E-04 | 9 | 8 am |

Meteorological data are obtained from various locations.  Table 4 summarizes the meteorological data used in this analysis.  While representative meteorological data is preferred, it is not always possible to determine which station is the most representative of the project site.  In these cases meteorological data from two nearest stations are used and results from both are presented.  US-EPA Guidelines recommend the latest five years of consecutive meteorological data for these types of analyses.  Five years of data are used where available.  In addition, it is requested to simulate air dispersion with meteorological data from South San Francisco, West Los Angeles, and Vernon.  In this case, the model results only reflect simulations from the facility with the highest emissions.

| Table 4 – Meteorological Data Summary |
| --- |
| Station | Abbreviation | Year | Anemometer Height Input to Model (m) | Avg. WS (m/s) | % Calms | Notes |
| Barrio Logan | BL | 2000 | 7 | 2.0 | 1 % | Data gathered at Logan Memorial for special study. |
| Lindbergh Airport | Lind | 1985-1989 | 10 | 3.6 | 7 % | San Diego Airport |
| Miramar Naval Air Station | Mir | 1967-1971 | 10 | 2.8 | 17 % | San Diego |
| Vernon | Vern | 1981 | 10 | 2.3 | 7 % | SCAQMD |
| West Los Angeles | WLA | 1981 | 10 | 1.5 | 19 % | SCAQMD |
| San Francisco Airport | SFO | 1985-1989 | 10 | 5.4 | 5 % |  |

## Results

The maximum above ambient annual average concentration is estimated to be

2.8x10-4  μg/m3 from the facility emitting 0.023 lbs/yr hexavalent chromium.  Figure 1 is a log-log plot showing the estimated above ambient annual average concentration of hexavalent chromium from all the facilities, as a function of downwind distance.  The downwind direction is selected as the direction of the maximum annual impact.  Table 5 shows the data presented in Figure 1.

### Figure 1 – Above Ambient Annual Average Hexavalent Chromium Concentrations

| Table 5 – Summary Table of Above Ambient Annual Average Concentration of Hexavalent Chromium (μg/m3) |
| --- |
| Source ID | Met. Data | Dir (deg) | Distance from source (m) |
|  |  |  | 20 | 30 | 40 | 50 | 100 | 200 | 500 | 1000 |
| Src1 | BL | 70 |  | 1.4E-04 | 9.5E-05 | 6.3E-05 | 1.6E-05 | 3.8E-06 | 5.5E-07 | 1.2E-07 |
| Src1 | SFO | 110 |  | 5.9E-05 | 4.2E-05 | 3.0E-05 | 9.4E-06 | 2.7E-06 | 4.7E-07 | 1.3E-07 |
| Src1 | WLA | 40 |  | 2.8E-04 | 1.9E-04 | 1.4E-04 | 4.2E-05 | 1.2E-05 | 2.0E-06 | 5.1E-07 |
| Src2 | BL | 40 | 1.4E-08 | 4.0E-08 | 7.1E-08 | 9.2E-08 | 9.8E-08 | 5.0E-08 | 1.1E-08 | 3.0E-09 |
| Src2 | SFO | 120 | 1.3E-07 | 1.9E-07 | 2.1E-07 | 2.0E-07 | 1.0E-07 | 4.0E-08 | 9.4E-09 | 2.9E-09 |
| Src2 | WLA | 40 | 1.3E-09 | 8.1E-09 | 2.2E-08 | 3.8E-08 | 7.0E-08 | 5.1E-08 | 1.5E-08 | 4.7E-09 |
| Src3 | Mir | 120 |  | 7.7E-07 | 9.9E-07 | 1.1E-06 | 7.8E-07 | 3.7E-07 | 1.1E-07 | 3.5E-08 |
| Src3 | SFO | 120 |  | 7.8E-07 | 1.2E-06 | 1.5E-06 | 1.3E-06 | 6.0E-07 | 1.6E-07 | 5.3E-08 |
| Src3 | WLA | 50 |  | 5.7E-07 | 7.5E-07 | 8.3E-07 | 9.4E-07 | 7.1E-07 | 2.9E-07 | 1.0E-07 |
| Src4 | BL | 100 |  |  | 9.7E-08 | 1.0E-07 | 6.3E-08 | 2.1E-08 | 3.7E-09 | 9.6E-10 |
| Src4 | SFO | 220 |  |  | 4.2E-08 | 4.5E-08 | 2.8E-08 | 9.5E-09 | 1.7E-09 | 4.5E-10 |
| Src4 | WLA | 50 |  |  | 1.8E-07 | 2.0E-07 | 1.4E-07 | 5.1E-08 | 9.3E-09 | 2.4E-09 |
| A blank cell indicates plume has yet to touchdown or the receptor is near the building wake effects and no calculation is made. |