Vapor Recovery Equipment Defects List

Adopted: September 23, 2002

Amended: [insert month day, year]

this page intentionally left blank

# Vapor Recovery Equipment Defects List

# Date of Issuance: September 23, 2002

| GVR All Systems/any E.O. |
| --- |
| equipment | defects | verification procedure |
| (a) system nozzles (b) nozzles | (1) any equipment defect which is identified in an Executive Order (E.O.) certifying a system pursuant to the Certification Procedures incorporated in Section 94011 of Title 17, California Code of Regulations (2) absence, improper installation, or disconnection of any component required to be used in the E.O.(s) that certified the system (3) installation or use of any uncertified component (4) dispensing rate greater than ten (10.0) gallons per minute (gpm) or less than the greater of five (5.0) gpm or the limit stated in the E.O. measured at maximum fuel dispensing (5) phase I vapor poppet inoperative (1) nozzle automatic liquid shutoff mechanisms which malfunction in any manner | as set forth in the applicable E.O. direct observation direct observation when determined as part of any ARB approved test method or direct measurement for 6030 seconds minimum direct observation EPO No. 26-F-1/direct observation |

Each defect in the tables in this list has a specific alphanumeric identification.  Every identification has three parts:  i) the executive order number for the table on which the defect appears (or GVR-general vapor recovery-for this “All Systems/any E.O.” page only), ii) a sequential letter for the equipment, with which the defect is associated, and iii) a sequential number for the defect itself.  As the “equipment” column in the table changes, the defect number sequence that is associated with the specific equipment begins again with one (“(1)”).  The same is true for the equipment letter.  At the start of a new table, the first identifying letter associated with the first equipment listed will be an “a”, the second a “b”, and so on.  The Executive Order number (part i) is comprised of the characters which proceed the literal description of the system.

For example:  the identification for the defect above which is written “installation or use of any uncertified component” is “GVR(a)(3)” and the last defect on the next table (page 2) is

“G-70-7(d)(1)”.

| G-70-7 series Hasstech VCP-2 and VCP-2A |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) hoses (c) processing unit (d) collection unit | (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) system not in compliance with the static pressure decay test criteria * (3) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) defective vapor valve (1) any coaxial hose with a perforation exceeding one-eighth (0.13) inch diameter (2) any coaxial hose with slits or tears in excess of one-fourth (0.25) inch in length (1) three consecutive unsuccessful attempts to ignite the incinerator which occur at least two hours after a bulk delivery * (2) unit does not activate when the system pressure reaches or exceeds two (2.0) inches water column and occurs at least two hours after a bulk delivery * (3) emissions which exceed Ringelmann one-half (½ ) or ten percent (10%) opacity and not attributable to a bulk delivery * (4) vapor processing unit inoperative * (1) vacuum producing device inoperative * | direct observation TP201.3 or equivalent TP201.5 or equivalent TP201.4 or equivalent GDF-01/GDF-03 direct measurement/ observation direct measurement/ observation direct measurement/ observation/system monitor observation direct measurement using storage tank pressure device Method 9 direct observation direct observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-14 series Red Jacket | G-70-17 series Emco Wheaton | G-70-23 series Exxon |
| --- | --- | --- |
| G-70-25 series Atlantic Richfield | G-70-33 series Hirt | G-70-36 series OPW |
| G-70-38 series Texaco | G-70-48 series Mobil | G-70-49 series Union |
| G-70-52 series Red Jacket, Hirt | G-70-53 series Chevron | G-70-78 series EZ-flow rebuilds |
| G-70-107 series Rainbow rebuilds | G-70-125 series Husky Model V | G-70-127 series OPW 111V |
| G-70-134 series EZ-flow rebuilds | G-70-139 series Hirt | G-70-170 series EZ-flow rebuilds |
| equipment | defects | verification procedure |
| (a) nozzles (b) hoses (c) processing unit (d) vapor return lines | (1) any nozzle boot torn in one or more of the following manners: a triangular-shaped or similar tear one-half (0.50) inch or more on any side, or hole one-half (0.50) inch or more in diameter, or slit one (1.0) inch or more in length (2) any faceplate or flexible cone damaged in the following manner: for balance nozzles and for nozzles for aspirator and eductor assist type systems, damage such that the capability to achieve a seal with a fill pipe interface is affected for one-fourth (0.25%) of the circumference of the faceplate (accumulated) (3) flexible cone damaged in the following manner: for booted type nozzles for vacuum assist-type systems, more than one-fourth (0.25%) of the flexible cone missing (4) insertion interlock mechanism which will allow dispensing when the bellow is uncompressed (1) any coaxial balance hose with 100 ml or more liquid in the vapor path (2) any hose with a visible opening (1) vapor processing unit inoperative * (1) pressure drop through the vapor path exceeds by a factor of two or more requirements specified in the Executive Order(s) that certified the system | direct measurement/ observation direct measurement/ observation direct measurement/ observation direct observation/ GDF-09 direct measurement direct observation direct observation TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

The identification scheme for defects listed in this table is the same three part alphanumeric identification (see page 1) as the other tables.  However, the correct executive order number will be the one for the specific system in question.  For example: the identification for the defect above which is written “any hose with a visible opening” will begin “G-70-“ and end with “(b)(2).”  On the Atlantic Richfield system it will be “G-70-25(b)(2)”, on the Texaco system it will be “G-70-38(b)(2)”, and so on.

| G-70-118 series Amoco V-1 |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) Husky V-1 nozzle (c) OPW 11-VAA nozzle | (1) defective vapor valve (2) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (3) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (4) system not in compliance with the static pressure decay test criteria * (5) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (1) efficiency compliance device (ECD) damaged such that at least one eighth (0.13%) of the diameter is missing (2) less than two unblocked vapor holes (1) any ECD damaged such that a slit from the outer to inner edge exists (2) less than three unblocked vapor holes | GDF-01/GDF-032 TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent direct measurement/ observation direct observation direct measurement/ observation direct observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-150 series Marconi (Gilbarco)Vapor Vac |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) Catlow ICVN nozzle (c) Emco Wheaton A4505 nozzle (d) Emco Wheaton A4500 nozzle (e) Husky V34 6250 nozzle (f) Husky V3 6201 nozzle (g) OPW 11VAI nozzle (h) OPW12VW nozzle | (1) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded defective vapor valve (3) system not in compliance with the static pressure decay test criteria * (4) both booted and unbooted nozzle types connected to the same vapor pump (5) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (1) less than three unblocked vapor holes (2) defective vapor valve (3) efficiency compliance device slit from base to the rim (1) less than three unblocked vapor holes (2) defective vapor valve (3) one-eighth (0.13%) of vapor guard circumference missing (1) less than three unblocked vapor holes (1) a one and one-half (1.5) inch or greater slit in vapor splash guard (2) any hole greater than three-eighths (0.38) inch in vapor splash guard (3) defective vapor valve (1) all vapor holes blocked (1) less than four unblocked vapor holes (1) all vapor holes blocked (2) defective vapor valve (3) vapor escape guard with three-fourths (0.75%) of the circumference missing | TP201.4 or equivalent direct observation GDF-01/GDF-03 TP201.3 or equivalent direct observation TP201.5 or equivalent direct observation GDF-01/GDF-02 direct observation direct observation GDF-01/GDF-02 direct measurement/ observation direct observation direct measurement/ observation direct measurement/ observation GDF-01/GDF-02 direct observation direct observation direct observation GDF-01/GDF-02 direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-153 series Dresser/Wayne Vac |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) OPW 11VAI and Husky V34 6200-4 nozzles (c) Husky V34 6200 nozzle (d) Husky V34 6200 and V34 6250 nozzles (e) Emco Wheaton A4505 nozzle (f) Catlow ICVN and Richards Astrovac nozzles (g) OPW 12VW nozzle | (1) any splash guard that interferes with the operation of a vapor escape guard (VEG) or vapor splash guard (VSG) unit (2) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (3) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (4) system not in compliance with the static pressure decay test criteria * (5) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (6) defective vapor valve (1) less than two unblocked vapor holes (2) any VEG damaged such that at least one-eighth (0.13%) of the circumference is missing (1) less than two unblocked vapor holes (1) any VSG damaged such that at least a one and one-half (1.5) inch slit has developed (2) any VSG flange portion that does not make contact with or cover the entire fill-pipe opening (3) any VSG with a hole greater than three-eighths (0.38) inch (1) less than three unblocked vapor holes (2) any vapor guard (VG) damaged such that at least one-eighth (0.13%) of the circumference is missing (1) less than three unblocked vapor holes (2) any efficiency compliance device damaged with a slit from the base to the rim (1) all vapor holes blocked (2) any VEG damaged such that at least three-quarters (0.75%) of the circumference is missing | direct measurement/ observation TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent GDF-01/GDF-032 direct observation direct measurement/ observation direct observation direct measurement/ observation direct measurement/ observation direct measurement/ observation direct observation direct measurement/ observation direct observation direct observation direct observation direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-154 series Tokheim MaxVac |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles (b) OPW 11VAI and Husky V34 6200-5 nozzles (c) Husky V34 6200 and V34 6250 nozzles (d) Emco Wheaton A4505 (e) Catlow ICVN and Richards Astrovac (f) system | (1) defective vapor valve (1) efficiency compliance device (ECD) damaged such that at least one-fourth (0.25%) of the circumference is missing (1) less than two unblocked vapor holes (2) vapor splash guard (VSG) damaged such that at least a one and one-half (1.5) inch slit has developed (3) VSG damaged such that greater than a three-eighths (0.38) inch hole has developed (1) less than seven unblocked vapor holes (1) less than four unblocked vapor holes (2) any nozzle with an ECD damaged with at least one-fourth (0.25%) of the circumference missing (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | GDF-01/GDF-032 direct measurement/ observation direct observation direct measurement/ observation direct measurement/ observation direct observation direct observation direct measurement/ observation TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-159 series Saber nozzle for Gilbarco (Marconi) Vapor Vac and WayneVac |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles (b) system | (1) a fill guard damaged such that at least one-fourth (0.25%) of the outer edge of the guard is missing (2) less than four unblocked vapor holes on the Gilbarco (Marconi) systems (3) less than two unblocked vapor holes on the WayneVac systems (4) defective vapor valve on the WayneVac systems (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | direct measurement/ observation direct observation direct observation GDF-01/GDF-032 TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-163 series OPW Vapor EZ |
| --- |
| Equipment | defects | verification procedure |
| (a) nozzles (b) system | (1) efficiency compliance device damaged such that at least one-eighth (0.13%) of the diameter is missing (2) less than three unblocked vapor holes (3) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | direct measurement/ observation direct observation GDF-01/GDF-032 TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-164 series Hasstech VCP-3A |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) OPW 11VAI steel spout (c) OPW 11VAI aluminum spout (d) Husky V3 6201 nozzle (e) Husky V34 6200-8 nozzle (f) Emco Wheaton A4500 nozzle (g) collection unit (h) processing unit (i) ECS-1 electronic control and status panel | defective vapor valve (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) system not in compliance with the static pressure decay test criteria * (3) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (1) less than six unblocked vapor collection holes (2) defective vapor valve (1) less than four unblocked vapor collection holes (2) defective vapor valve (1) all vapor collection holes blocked (1) all vapor collection holes blocked (2) defective vapor valve (1) any visible puncture or tear of the vapor guard/vapor seal assembly (2) less than three unblocked vapor collection holes (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) dispensing when the collection unit is disabled * (3) normal operating level at the inlet of the collection unit less than thirty (30) inches water column vacuum * (1) emissions which exceed Ringelmann one-half (½) or ten percent (10%) opacity and not attributable to a bulk delivery * (2) twenty (20) consecutive unsuccessful attempts to ignite the process unit * (3) dispensing when the process unit is disabled * (4) processing unit inoperative * (1) ratio of process unit/solenoid valve time less than nine tenths (0.90) * | GDF-01/GDF-03 direct observation TP201.3 or equivalent TP201.4 or equivalent direct observation GDF-01/GDF-02 direct observation GDF-01/GDF-02 direct observation direct observation GDF-01/GDF-02 direct observation direct observation TP201.5 or equivalent direct observation/ system monitor observation direct measurement/ observation Method 9 direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct observation direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-165 series Healy Model 600 |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles (b) system (c) central vacuum unit | (1) any nozzle with a vapor guard missing, damaged such that a slit from the outer edge of the open end flange to the spout anchor clamp, or which has equivalent cumulative damage (2) any nozzle which has fewer than four unblocked vapor collection holes (3) defective vapor valve (4) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (5) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (1) system not in compliance with the static pressure decay test criteria * pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (1) dispensing when the central vacuum unit is disabled * (2) vacuum level outside of the range specified in G-70-165 for more than fifteen (15) seconds (Approval Letter 97-20), measured while dispensing is occurring * (3) product dispensed when the vapor return line valve is closed | direct observation direct observation GDF-01/GDF-032 EO G-70-183 Exhibit 2 vapor valve test or equivalent TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation/TP201.5 |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-169 series Franklin Electric Intellivac |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) OPW 11VAI nozzle (c) Husky V34 6250 nozzle | (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (5) defective vapor valve (1) efficiency compliance device damaged such that at least one-fourth (0.25%) of the circumference is missing (2) fewer than two unblocked vapor collection holes (1) any nozzle with a vapor splash guard (VSG) damaged such that at least one and one-half (1.5) inch slit has developed (2) any VSG damaged such that greater than a three-eighths (0.38) inch hole has developed | TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent GDF-01/GDF-032 direct measurement/ observation direct observation direct measurement direct measurement |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-175 series Hasstech VCP-3A |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) OPW 11VAI steel spout (c) OPW 11VAI aluminum spout (d) Emco Wheaton A4500 nozzle (e) Husky V3 6201 nozzle (f) Husky V34 6200-8 dispenser (g) collection unit (h) processing unit (i) ECS-1 electronic control and status panel | (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) system not in compliance with the static pressure decay test criteria * (3) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (1) less than six unblocked vapor collection holes (1) less than four unblocked vapor collection holes (1) fewer than three unblocked vapor collection holes (2) any visible puncture or tear of the vapor guard/vapor seal assembly (1) all vapor collection holes blocked (1) all vapor collection holes blocked (2) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) dispensing when the collection unit is disabled * (3) normal operating level at the inlet of the collection unit less than thirty (30) inches water column vacuum * (1) twenty (20) consecutive unsuccessful attempts to ignite the processing unit * (2) emissions which exceed Ringelmann one-half (½) or ten percent (10%) opacity and not attributable to a bulk delivery * (3) dispensing when the processing unit is disabled * (4) processing unit inoperative * (1) ratio of process unit/solenoid valve time less than nine tenths (0.90) * | direct observation TP201.3 or equivalent TP201.4 or equivalent direct observation direct observation direct observation direct observation direct observation direct observation GDF-01/GDF-032 TP201.5 or equivalent direct observation/ system monitor observation direct measurement/ observation direct measurement/ observation/ system monitor observation Method 9 direct measurement/ observation/system monitor observation direct observation direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-177 series Hirt VCS400-7 |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) OPW 11VA-29 nozzle (c) hoses | (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (3) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (4) processing unit inoperative * (1) defective vapor valve (2) less than five unblocked vapor collection holes (1) any visible puncture or tear equivalent to a diameter of 0.136 inches or greater | direct observation TP201.4 or equivalent TP201.5 or equivalent direct observation GDF-01/GDF-032 direct observation direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-179 series Catlow ICVN-VI |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles (b) system | (1) efficiency compliance device damaged such that at least three-fourths (0.75%) of the diameter is missing (2) any nozzle which has less than four unblocked vapor collection holes (3) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | direct measurement/ observation direct observation GDF-01/GDF-032 TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-181 series Hirt VCS400-7 AGT |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) OPW 11VA-29 nozzle (c) hoses | (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) pressure drop through the system exceeds one-half (0.50) inch water column at sixty cubic feet per hour (60 CFH) (3) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (4) processing unit inoperative * (1) defective vapor valve (2) less than five unblocked vapor collection holes (1) any visible puncture or tear equivalent to a diameter of 0.136 inches or greater | direct observation TP201.4 or equivalent TP201.5 or equivalent direct observation GDF-01/GDF-02 direct observation direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-183 series Healy/Franklin Vac Assist |
| --- |
| equipment | defects | Verification procedure |
| (a) nozzles (b) system | (1) a vapor guard damaged such that a slit exists from the outer edge of the open end flange to the spout anchor clamp (2) any nozzle which has less than four unblocked vapor collection holes (3) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | direct observation direct observation GDF-01/GDF-032 EO G-70-183 Exhibit 2 vapor valve test or equivalent TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-186 series Healy Model 400 ORVR |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles system (b) central vacuum unit (c) system | (1) any operating pressure range at the nozzle boot/fill-pipe interface less than one-half (0.50) inch water column vacuum or greater than one-fourth (0.25) inch water column pressure (2) defective vapor valve system not operating within the vacuum level range as per G-70-186 (1) product dispensed when the central vacuum unit is inoperative or disabled * (2) system does not achieve an operating vacuum of sixty-five (65) inches water column for three consecutive dispensings under normal operating conditions * (3) system operates at a vacuum less than sixty-five (65) inches water column over a one hour period * (4) vacuum level dropping below sixty (60) inches water column for more than three seconds after the system has reached sixty-five (65) inches water column, while dispensing is occurring * (5) vacuum level above ninety (90) inches water column while dispensing is occurring * (6) product dispensing when the non-restrictive ball valve installed in the vapor return line is closed * (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) system not in compliance with the static pressure decay test criteria * (3) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (4) any venting through system monitor vent in excess of ten hours in any calendar day not attributable to a Phase I fuel delivery * | EO G-70-186 Exhibit 5 test GDF-01/GDF-032 EO G-70-191 Exhibit 2 vapor valve test or equivalent direct measurement/ observation/system monitor observation direct measurement/ observation/TP201.5 or equivalent system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation direct observation TP201.3 or equivalent TP201.4 or equivalent observation/system monitor observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-187 series Healy Model 400 ORVR AGT (AST) |
| --- |
| equipment | defects: | verification procedure |
| (a) nozzles (b) central vacuum unit (c) system Phase II system | (1) any operating pressure range at the nozzle boot/fill-pipe interface less than one-half (0.50) inch water column vacuum or greater than one-fourth (0.25) inch water column pressure (2) defective vapor valve (3) any nozzle boot with a concatenation of all tears greater than one-half (0.50) inch in length system vacuum less than sixty-five (65) inches or greater than eighty-five (85) inches water (1) product dispensed when the central vacuum unit is inoperative or disabled * system does not achieve an operating vacuum of sixty-five (65) inches water column within fifteen (15) seconds after the system is energized (2) system does not achieve an operating vacuum of sixty-five (65) inches water column for three consecutive dispensing episodes * (3) system does not achieve an operating vacuum of sixty-five (65) inches water column within a one hour period for any single dispensing episode * (4) vacuum level dropping below sixty (60) inches water column for more than three seconds after the system has reached sixty-five (65) inches water column, while dispensing is occurring * (5) vacuum level above ninety (90) inches water column while dispensing is occurring * (6) product dispensing when the non-restrictive ball valve installed in the vapor return line is closed * (1) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (2) system not in compliance with the static pressure decay test criteria * (3) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (4) any venting through system monitor vent in excess of ten hours in any calendar day not attributable to a Phase I fuel delivery * | EO G-70-187 Exhibit 5 test GDF-01/GDF-02 EO G-70-191 Exhibit 2 vapor valve test or equivalent direct measurement/ observation direct measurement/ observation direct measurement/ observation/TP201.5 or equivalent system monitor observation direct measurement/ observation direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation/system monitor observation direct measurement/ observation direct observation TP201.3 or equivalent TP201.4 or equivalent direct measurement/ observation/system monitor observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-188 series Catlow ICVN w/Gilbarco (Marconi) VaporVac System |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles (b) system | (1) ECD damaged such that at least three-fourths (0.75%) of the diameter is missing (2) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | direct measurement/ observation GDF-01/GDF-032 TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-191 series Healy ORVR |
| --- |
| equipment | defects | verification procedure |
| (a) nozzles (b) system | (1) any nozzle with a vapor collection boot which has one-half (0.50%) of the mini-boot faceplate or greater missing (2) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) | direct measurement/ observation GDF-01/GDF-032 EO G-70-191 Exhibit 2 vapor valve test or equivalent TP201.5 or equivalent direct observation TP201.3 or equivalent TP201.4 or equivalent |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-193 series Hill-Vac |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) nozzles (c) jet pump (d) Liquid drop out pot | (1) fillpipe gauge pressure less than negative one (–1.0) inch or greater than two (2.0) inches water column (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) pressure drop through the system exceeds one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (1) a boot with any tear exceeding one-half (0.50) inch (2) faceplate damage such that the fillpipe interface is adversely affected for twenty-five percent (25%) or more of the circumference of the faceplate (1) dispensing of gasoline when either jet pump is disabled (2) failure to achieve operating vacuum of thirty-five (35) inches water column within five seconds after the system is activated, for three consecutive dispensing episodes (3) a vacuum level below fifteen (15) inches water column for more than three seconds after the system has reached thirty-five (35) inches water column while dispensing (4) a vacuum level above eighty-five (85) inches water column measured while dispensing to non-ORVR vehicles (5) product dispensing when any ball valve installed at the vapor return line connection to each Healy Model 100 jet pump is closed (1) opening drain valve at anytime other than when repair operations are underway (2) product dispensing when any ball valve installed at the liquid drop pot in the liquid removal line is closed | direct measurement/ observation direct observation TP201.3 or equivalent TP201.4 or equivalent direct measurement/ observation direct measurement/ observation direct observation direct measurement/ observation direct measurement/ observation direct measurement/ observation direct measurement/ observation direct observation direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-196 series SaberVac |
| --- |
| equipment | Defects | verification procedure |
| (a) Husky 605104 nozzle (b) system | (1) vapor splash guard (VSG) with a one and one-half (1.5) inch or larger slit (2) VSG with a three-sixteenths (0.19) inch or larger hole (3) the VSG flange portion doesn’t make contact with entire fillpipe opening (4) defective vapor valve (1) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard as described in G-70-196 (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) underground storage tank gauge pressure greater than two inches water column over an extended period as defined by E.O. G-70-196 Exhibit 2 * (5) pressure drop through system exceeding one-half (0.50) inch water column at sixty standard cubic footfeet per hour (60 SCFH) (6) dispensing of product from any fueling point associated with a disconnected vapor line | Direct measurement/ observation Direct measurement/ observation direct observation GDF-01/GDF-032 as described in G-70-196 direct observation TP201.3 or equivalent direct measurement/ observation TP201.4 or equivalent direct measurement/ observation |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

| G-70-204 series Gilbarco Vapor Vac/OPW Vaporsaver |
| --- |
| equipment | defects | verification procedure |
| (a) system (b) Catlow ICVN nozzle (c) Emco Wheaton A4505 nozzle (d) Husky V34 6250 nozzle (e) OPW12VW nozzle (f) vapor processor | (1) pressure drop through the system exceeds one-half (0.50) inch water column at sixty cubic feet per hour (60 CFH) (2) any fueling point associated with a vapor line disconnected and open to the atmosphere, including all fueling points at the facility if vapor lines are manifolded (3) system not in compliance with the static pressure decay test criteria * (4) any grade of a fueling point not capable of demonstrating an air to liquid ratio compliance with its performance standard (5) defective vapor valve (1) less than three unblocked vapor holes (2) efficiency compliance device slit from base to the rim (1) less than three unblocked vapor holes (2) one-eighth (1/8) of vapor guard circumference missing or equivalent cumulative damage (1) a one and one-half (1.5) inch or greater slit in vapor splash guard or equivalent cumulative damage (2) any hole greater than three-eighths (3/8) inch in vapor splash guard or equivalent cumulative damage (1) all vapor holes blocked (2) vapor escape guard with three-fourths (3/4) of the circumference missing or equivalent cumulative damage (1) vapor processor inoperative * | TP201.4 or equivalent direct observation TP201.3 or equivalent TP201.5 or equivalent GDF-01/GDF-02 direct observation direct observation direct observation direct measurement/ observation direct measurement/ observation direct measurement/ observation direct observation direct measurement/ observation direct observation/ G-70-204 Exhibit 2 |

* When the identified defect is detected in the listed equipment, the defect determination applies to all affected interrelated systems (which may include all systems at the motor vehicle fueling operation).

Defect Identification Methods Used In the Verification Procedure Column

1. TP201.5:	Determination (by Volume Meter) of Air to Liquid (A/L) Volume Ratio of

Vapor Recovery Systems of Dispensing Facilities, Adopted April 12, 1996

2. TP201.4:	Determination of Dynamic Pressure Performance of Vapor

Recovery Systems of Dispensing Facilities

3. TP201.3:	Determination of Two-Inch WC Static Pressure Performance of Vapor

Recovery Systems of Dispensing Facilities

4. GDF-01:  	Bag Test for Multi-Nozzle Vacuum Assist Systems

5. GDF-03:	Pressure Integrity Performance Verification for Vacuum Assist Systems [Squeeze Bulb Test]

65. Method 9:	40 Code Federal Regulations Part 60 Appendix A:  Reference Method 9/

EPA Section 3.12 Visible Determination of the Opacity of Emissions from Stationary Sources

76. G-70-186-187 Exhibit 5:  Fillneck Vapor Pressure Regulation Fueling Test

87. EPO No. 26-F-1:  Vapor Recovery Systems Field Compliance Testing

98. Storage Tank Pressure Device:  described and shown in TSD Appendix 6

9. GDF-02:	Bag Test for Single-Nozzle Vacuum Assist Systems

# 10. GDF-09:	Phase II Balance System Nozzle Insertion Interlock Operation Determination